## Slide 1
AERO / PROJECT RESOURCE PACK
Aero Ground
Station
Hardware implementation, communication
and system architecture
3-inch quadcopter | ArduCopter | ELRS | Laptop AI
26 October 2026 • Evidence-based project documentation
Notes: A comprehensive project resource pack. The PDF carries full engineering explanations, source links and acceptance criteria. Slides are editable; additional detail is in speaker notes. Hardware behavior that has not been validated is marked as pending.

## Slide 2
AERO / 01
Project purpose and system boundary
A supervised observation and rescue-review prototype
Hardware implementation | 26 October 2026
2 / 38
01
ArduCopter closes the flight-control loop onboard.
02
The laptop combines video, AI, maps, incident evidence and bounded route feedback.
03
A human pilot retains takeoff, landing, flight-mode and takeover authority.
Notes: A supervised observation and rescue-review prototype
Aero Ground Station combines a small ArduCopter aircraft, an ELRS radio link, an independent analog FPV video link and a Windows laptop. The laptop displays telemetry and video, assists search planning, runs person detection and records candidate rescue incidents. The flight controller remains responsible for stabilization and onboard protective behavior.
The project is intended to assist a trained pilot and a rescue operator. A detector box means a possible person in an image; it does not confirm a survivor, identity, medical condition or exact ground coordinates. A reviewed search route is a request for bounded movement, not evidence that the airspace or terrain is clear.
This pack documents the current application and the hardware discussed during commissioning. It is a technical explanation and implementation record, not a declaration that the aircraft is flight-ready. It includes architecture, interface contracts, UML views, parameter provenance and remaining acceptance work.
Onboard: sensing, estimation, motor control and flight failsafes.
On the laptop: interface, AI, route feedback, event storage and review.
Human authority: takeoff, landing, mode selection, takeover and evidence verification.
Documentation date: 26 October 2026. Hardware confirmations are historical observations from this project conversation.
S11 | Application repository | https://github.com/rithinreddy0/aero-ground-station
S12 | Team AURA source, pinned integration revision | https://github.com/7-Azhar/major_project/tree/d50829119b598e5b32b352f384fdd25aca367f08

## Slide 3
AERO / 02
Evidence and current implementation status
Separate confirmed behavior, implemented software and unresolved integration
Hardware implementation | 26 October 2026
3 / 38
01
User-reported: sensor calibration, radio modes and corrected motor tests.
02
Implemented: telemetry, video upload, AI review, tracking and incident storage.
03
Pending evidence: reliable GPS fix, live capture hardware, battery calibration and flight validation.
Notes: Separate confirmed behavior, implemented software and unresolved integration
Mission Planner screenshots identified ArduCopter 4.7.1 on SpeedyBeeF405AIO and Mission Planner 1.3.83. The user reported a 4S 650 mAh battery, 3-inch props, a GM10 Mini V3 GPS and iFlight analog goggles. The exact ELRS receiver, transmitter-module firmware, camera, VTX and motor KV remain unrecorded.
The user confirmed radio channels, mode changes, corrected motor order and rotation, and disarmed radio-failsafe detection/recovery. Those are useful bench observations. They do not prove stable flight, correct GPS navigation, an obstacle-safe RTL path or airborne failsafe recovery.
The last recorded software validation on 16 October reported 46 passing tests and actual VisDrone inference on team footage. GPS remained unresolved in the conversation. The analog receiver/capture options were investigated, but purchase and live capture were not confirmed.
Evidence level | Examples
User-confirmed bench | Mode switches, motor order/direction, RC-loss message
Software verified | Upload, decode, AI adapter, policy tests, local playback
Unresolved | GPS fix/heading, current sensing, RF command/latency tests
Proposed only | RC805/EasyCAP purchase, speaker and sensor additions
Treat the saved parameter patches as commissioning history. A fresh FC export is needed to prove the present onboard values.
S11 | Application repository | https://github.com/rithinreddy0/aero-ground-station
S12 | Team AURA source, pinned integration revision | https://github.com/7-Azhar/major_project/tree/d50829119b598e5b32b352f384fdd25aca367f08

## Slide 4
AERO / 03
Hardware component inventory
Known parts, roles and missing identifiers
Hardware implementation | 26 October 2026
4 / 38
01
SpeedyBee F405 AIO V1 running ArduCopter; 3-inch propellers.
02
4S 650 mAh LiPo, marked 95C; motor/KV and aircraft mass still need recording.
03
GM10 Mini V3 GPS, ELRS radio link and analog FPV equipment.
04
Receiver model, ELRS versions, camera/VTX and compass variant remain to be identified.
Notes: Known parts, roles and missing identifiers
The AIO is both a flight-control board and an integrated ESC assembly; it is not the same thing as the entire aircraft. The frame, motors, propellers, power wiring, receiver, navigation sensor and video system complete the aircraft. Each component needs a recorded model, supply requirement, mounting orientation and connection.
Keep a photographed bill of materials with serial numbers where useful. Do not substitute a component solely because its connector fits. Matching protocol, voltage, pinout, frequency and mechanical clearance matters more than a shared product category.
Component | Project record / role
Flight controller / ESC | SpeedyBee F405 AIO V1; ArduCopter + four motor outputs
Propulsion / battery | 3-inch props; 4S 650 mAh 95C; motor KV unconfirmed
Navigation | Flywoo GM10 Mini V3; UART5; compass variant to confirm
RC / telemetry | ELRS aircraft RX + TX module; RadioMaster Pocket reported in notes
FPV observation | Analog camera/VTX + iFlight goggles; exact models unknown
Ground computer | Windows laptop; Mission Planner + local Python application
Video-to-USB hardware | UVC receiver OR analog VRX plus capture; not confirmed purchased
S01 | ArduPilot: SpeedyBee F405 AIO board support | https://ardupilot.org/copter/docs/common-speedybeef405aio.html
S03 | Flywoo: GOKU GM10 Mini V3 GPS specifications | https://flywoo.net/products/goku-gm10-mini-v3-gps
S11 | Application repository | https://github.com/rithinreddy0/aero-ground-station

## Slide 5
AERO / 04
AIO and ArduPilot responsibilities
The autopilot firmware lives on the flight controller
Hardware implementation | 26 October 2026
5 / 38
01
AIO: processor, IMU, barometer, regulators and electrical interfaces.
02
ArduCopter: state estimation, stabilization, motor mixing and onboard failsafes.
03
Mission Planner: setup, parameter readback, diagnostics and log review.
04
Custom application: supervised observations and constrained movement requests.
Notes: The autopilot firmware lives on the flight controller
ArduPilot is the autopilot software family. ArduCopter is its multirotor firmware, installed on the AIO. It reads inertial/navigation sensors, estimates attitude and position, interprets flight modes and produces motor commands. Integrated ESCs translate those commands into the switching currents that drive brushless motors.
Mission Planner is a ground application used to configure, inspect and command ArduPilot. It is not firmware inside the radio and is not a compulsory forwarding process between our app and the aircraft. Our application can communicate directly with the same autopilot through its own MAVLink adapter.
The SpeedyBee board support page is the reference for the ArduPilot target and board-specific mappings. The AIO has no built-in compass; an external device, if present, must be identified separately. Firmware limitations on an F405 target mean an optional ArduPilot feature should be checked before designing around it.
AIO hardware provides computing, sensor interfaces and ESC connections.
ArduCopter provides flight behavior; ELRS transports control and data.
The laptop never substitutes for the onboard attitude controller.
S01 | ArduPilot: SpeedyBee F405 AIO board support | https://ardupilot.org/copter/docs/common-speedybeef405aio.html
S17 | SpeedyBee manufacturer board manual | https://spcdn.speedybee.cn/cdn/58507926851031040.pdf

## Slide 6
AERO / 05
Power, propulsion and energy flow
Separate battery power, regulated electronics power and motor signals
Hardware implementation | 26 October 2026
6 / 38
01
The battery feeds propulsion; regulated rails supply the FC, GPS and receiver.
02
DShot signals command the ESC; motor phase wires carry propulsion power.
03
4S reaches 16.8 V when full. A 12 V-only receiver needs suitable regulated power.
04
Endurance requires measured hover current, aircraft mass and usable battery capacity.
Notes: Separate battery power, regulated electronics power and motor signals
The 4S pack supplies the aircraft power input. Its nominal voltage is 14.8 V and standard full-charge voltage is 16.8 V. The recorded 650 mAh capacity corresponds to 9.62 Wh nominal energy (14.8 x 0.65), not a prediction of usable flight energy or endurance. The 95C label is not a measured system current limit.
The ESC power stage drives the four motors. Regulated rails power flight electronics and suitable peripherals. A UART is a data interface and does not define a peripheral supply voltage. Check the board/manual and the exact receiver or camera before using a power pad.
Battery monitoring has three different roles: measuring voltage/current, estimating consumed capacity and triggering protective actions. USB-only bench power does not provide a valid flight-pack voltage. A plausible voltage display still needs comparison with a charger or meter; percentage estimates depend on capacity/current calibration.
No endurance claim is justified until mass, hover current and usable capacity are measured.
Do not power a 12 V-only RC805 directly from a 4S pack.
Disconnect power before changing motor wires; keep props removed for setup.
Historical thresholds: low 14.4 V, critical 14.0 V and arming minimum 14.7 V. These were initial project choices, not universally valid battery specifications.
S07 | ArduPilot: battery failsafe | https://ardupilot.org/copter/docs/failsafe-battery.html
S17 | SpeedyBee manufacturer board manual | https://spcdn.speedybee.cn/cdn/58507926851031040.pdf

## Slide 7
AERO / 06
GPS and compass integration
UART position data and I2C heading data are separate interfaces
Hardware implementation | 26 October 2026
7 / 38
01
GNSS position: GPS TX -> AIO R5; GPS RX <- AIO T5; check supply and ground.
02
A compass, if fitted, communicates separately over SDA/SCL.
03
A powered LED does not prove a 3D fix or valid EKF position.
04
Verify GPS status, satellites, HDOP and message age in telemetry.
Notes: UART position data and I2C heading data are separate interfaces
The user identified the GPS as GM10 Mini V3 and confirmed connection to UART5. The intended data wiring is GPS TX to AIO R5 and GPS RX to AIO T5, plus correct power and common ground. The project changed SERIAL5_BAUD from 57 to 115 (115200 baud); SERIAL5_PROTOCOL=5, GPS1_TYPE=1 and GPS_AUTO_CONFIG=1 already matched.
The module LED colors alone did not establish a valid fix. A useful diagnosis needs fresh GPS_RAW_INT, fix type, satellite count and dilution/accuracy information. A stationary open-sky test, antenna orientation, stable supply, serial communication and RF interference should be investigated systematically rather than changing several parameters at once.
A compass, if included in the module variant, uses separate SDA/SCL connections. The historical parameter export detected an external compass, but this does not establish that it is part of this exact GM10 or that its mounting orientation is correct. Verify level headings in known directions. Do not apply a printed rotation label blindly.
GPS fix was still unresolved at the end of hardware troubleshooting. Do not represent Loiter, RTL, GUIDED navigation or fence readiness as demonstrated.
S01 | ArduPilot: SpeedyBee F405 AIO board support | https://ardupilot.org/copter/docs/common-speedybeef405aio.html
S03 | Flywoo: GOKU GM10 Mini V3 GPS specifications | https://flywoo.net/products/goku-gm10-mini-v3-gps
S10 | MAVLink: common message definitions | https://mavlink.io/en/messages/common.html

## Slide 8
AERO / 07
End-to-end system architecture
RC, MAVLink telemetry and video use different paths
Hardware implementation | 26 October 2026
8 / 38
RC + MAVLink RF
UART6 TX/RX
UDP / serial
via TX RF link
analog RF video
USB video
Pilot / radio
ELRS TX module
Aircraft ELRS RX
AIO + ArduCopter
stabilization / EKF
Laptop GCS
MP or custom app
TX Backpack Wi-Fi
or supported USB
FPV camera + OSD
analog VTX
5.8 GHz analog VRX
USB capture or UVC
Laptop video / AI
incidents / review
Telemetry is bidirectional. Video travels separately. The laptop bridge depends on the actual transmitter hardware.
Notes: RC, MAVLink telemetry and video use different paths
Read the three paths independently. Manual inputs originate at the pilot handset and arrive at ArduCopter through the ELRS aircraft receiver. MAVLink carries aircraft state in the opposite direction and carries supervised laptop requests toward the FC. Analog video originates in the FPV camera/VTX and needs its own compatible video receiver.
The radio and laptop bridge are ground equipment. The aircraft receiver is not the same component as the 5.8 GHz FPV receiver. The RF band and packet configuration of the installed ELRS hardware must be documented; do not assume they match the video link.
Telemetry is bidirectional. Video travels separately. The laptop bridge depends on the actual transmitter hardware.
S02 | ExpressLRS: native MAVLink setup and laptop bridging | https://www.expresslrs.org/software/mavlink/
S11 | Application repository | https://github.com/rithinreddy0/aero-ground-station

## Slide 9
AERO / 08
ELRS link and laptop bridging
Native MAVLink is different from ordinary CRSF telemetry
Hardware implementation | 26 October 2026
9 / 38
01
Native ELRS MAVLink carries RC plus bidirectional MAVLink over a supported RF setup.
02
The laptop may connect through a TX Backpack UDP bridge or supported transmitter USB.
03
Ordinary CRSF telemetry alone is not a general laptop MAVLink bridge.
04
Record the actual TX/RX models, firmware versions, bridge and serial settings.
Notes: Native MAVLink is different from ordinary CRSF telemetry
ExpressLRS is the RF control/data link between a compatible transmitter module and aircraft receiver. This project uses the native MAVLink path, which supports RC plus bidirectional telemetry with compatible hardware/firmware. Conventional CRSF telemetry on the handset is not automatically a laptop MAVLink connection.
For this AIO the project uses UART6 for the receiver, with SERIAL6_PROTOCOL=2 and SERIAL6_BAUD=460. Receiver TX connects to R6 and receiver RX to T6. The chosen stream rates and radio settings must fit the actual RF throughput. RSSI_TYPE=5 is the native-MAVLink configuration used here.
On the ground, a compatible TX Backpack can forward MAVLink over Wi-Fi, commonly to a UDP GCS endpoint. A supported external TX module may expose serial MAVLink over its own USB. The handset USB joystick socket is a different interface. The actual bridge used by this build remains to be recorded, so both supported alternatives are shown rather than claiming a specific one was verified.
Recorded application endpoint: udpin:0.0.0.0:14550. This is a configured receive address, not proof of a working wireless link.
S02 | ExpressLRS: native MAVLink setup and laptop bridging | https://www.expresslrs.org/software/mavlink/

## Slide 10
AERO / 09
Wiring and interface register
Record electrical connections separately from logical software links
Hardware implementation | 26 October 2026
10 / 38
01
UART5: GM10 GPS, with crossed TX/RX and correct regulated power.
02
UART6: aircraft ELRS receiver; confirm actual wiring and firmware transport.
03
I2C: separate external compass interface, only if the sensor is present.
04
USB: direct FC setup. RF video reaches the laptop through a separate capture path.
Notes: Record electrical connections separately from logical software links
Use pad labels from the exact AIO revision. TX/RX are crossed between devices because a transmitter output must feed the other device receiver input. Ground reference is required. Connector color order is not a substitute for labelled continuity checks.
The diagram deliberately does not claim a connector pin order. Consult the board and peripheral manuals before soldering. Keep antennas and sensitive GNSS/compass wiring clear of avoidable motor-current and RF interference sources, then verify behavior after final assembly.
Connection | Interface / intended direction
GPS TX / RX | TX -> R5; RX <- T5; UART5 GPS
ELRS receiver TX / RX | TX -> R6; RX <- T6; UART6 native MAVLink
External compass if fitted | SDA <-> SDA; SCL <-> SCL; I2C + correct supply
Laptop service connection | USB -> FC SERIAL0 MAVLink2; COM number is machine-specific
FC to integrated ESCs | DShot600; outputs 1-4 with project remapping
Camera / OSD / VTX | Analog video through appropriate board pads; supply separately verified
S01 | ArduPilot: SpeedyBee F405 AIO board support | https://ardupilot.org/copter/docs/common-speedybeef405aio.html
S02 | ExpressLRS: native MAVLink setup and laptop bridging | https://www.expresslrs.org/software/mavlink/
S17 | SpeedyBee manufacturer board manual | https://spcdn.speedybee.cn/cdn/58507926851031040.pdf

## Slide 11
AERO / 10
Aircraft interface diagram
Physical interfaces around the AIO
Hardware implementation | 26 October 2026
11 / 38
GPS TX -> R5
GPS RX <- T5
I2C, separate from GPS
RX TX -> R6
RX RX <- T6
DShot600 signals
SpeedyBee AIO
ArduCopter
GM10 GPS
TX / RX / 5V / GND
External compass
SDA / SCL, if fitted
ELRS receiver
TX / RX / power
Integrated 4-in-1 ESC
4 motors
Arrows summarize signal interfaces, not pin order or connector orientation. Check labels and voltage before soldering.
Notes: Physical interfaces around the AIO
The flight controller receives navigation and RC information while independently commanding propulsion. A power rail can be shared only within its verified rating; the data connectors do not imply that all peripherals tolerate the same voltage.
The firmware serial number is logical. In this board configuration UART5 is GPS and UART6 is the full bidirectional receiver link. Other boards or firmware targets can use different mappings.
Arrows summarize signal interfaces, not pin order or connector orientation. Check labels and voltage before soldering.
S01 | ArduPilot: SpeedyBee F405 AIO board support | https://ardupilot.org/copter/docs/common-speedybeef405aio.html
S17 | SpeedyBee manufacturer board manual | https://spcdn.speedybee.cn/cdn/58507926851031040.pdf

## Slide 12
AERO / 11
UML deployment diagram
Where hardware and software execute
Hardware implementation | 26 October 2026
12 / 38
SPI / I2C / UART
RC + MAVLink
Wi-Fi UDP or TX USB
USB service link
OR wireless MAVLink
<<device>> Aircraft
AIO: ArduCopter 4.7.1
<<device>> Sensors
IMU / barometer / GNSS
<<device>> Radio system
ELRS TX + receiver
<<device>> Windows laptop
Mission Planner / FastAPI / AI
Mission Planner and the custom application are peer GCS clients. Sharing an endpoint requires an intentional router.
Notes: Where hardware and software execute
Deployment assigns processes to physical devices. ArduCopter executes on the AIO; Mission Planner, FastAPI, OpenCV and PyTorch execute on the laptop. ELRS firmware executes on the transmitter module/receiver, and optional Backpack firmware executes on the compatible bridge hardware.
In ordinary commissioning only one GCS should own a serial or UDP receive endpoint. To run Mission Planner and the custom application simultaneously, use an explicitly configured MAVLink router/forwarder with distinct endpoints. Two applications competing for one COM port caused access-denied behavior during this project.
Mission Planner and the custom application are peer GCS clients. Sharing an endpoint requires an intentional router.
S02 | ExpressLRS: native MAVLink setup and laptop bridging | https://www.expresslrs.org/software/mavlink/
S11 | Application repository | https://github.com/rithinreddy0/aero-ground-station

## Slide 13
AERO / 12
Manual radio control and modes
A three-position mode switch plus separate auxiliary requests
Hardware implementation | 26 October 2026
13 / 38
01
Channel 6, three positions: 1000 Stabilize / 1500 Loiter / 2000 GUIDED.
02
Channel 5 high: RTL request. Channel 7 high: AltHold request.
03
Channel 8 high: Land request. Return auxiliary switches low after use.
04
Check all switch interactions on the bench; GPS-dependent modes need valid position.
Notes: A three-position mode switch plus separate auxiliary requests
Channel 6 is the main mode channel. At approximately 1000 it selects Stabilize, at 1500 Loiter and at 2000 GUIDED. The project assigns duplicate neighboring mode slots to make the intended three positions clear: FLTMODE1/2=0, FLTMODE3/4=5 and FLTMODE5/6=4.
Channel 5 high requests RTL (RC5_OPTION=4), channel 7 high requests AltHold (RC7_OPTION=70) and channel 8 high requests Land (RC8_OPTION=18). Channel 6 has no auxiliary function. Begin a mode check with the auxiliary switches low and test one request at a time. Do not assume simultaneous auxiliary switches have a priority order designed for this project.
Manual takeover means selecting an appropriate pilot-controlled mode. Moving sticks in GUIDED is not a general substitute for mode takeover. Stabilize uses manual throttle; Loiter needs a healthy position estimate; switching modes requires a pilot familiar with the resulting controls. The user confirmed mode changes, but a complete in-flight takeover test remains pending.
Parameter | Recorded assignment
FLTMODE_CH | 6
FLTMODE1 / 2 | 0 / 0: Stabilize
FLTMODE3 / 4 | 5 / 5: Loiter
FLTMODE5 / 6 | 4 / 4: GUIDED
RC5 / RC7 / RC8_OPTION | 4 RTL / 70 AltHold / 18 Land
S09 | ArduPilot: radio mode-switch configuration | https://ardupilot.org/copter/docs/common-rc-transmitter-flight-mode-configuration.html

## Slide 14
AERO / 13
Motor order and rotation
The corrected mapping differs from the original export
Hardware implementation | 26 October 2026
14 / 38
Front-left: D / Motor 3
Output 2: function 35
Clockwise
Front-right: A / Motor 1
Output 1: function 33
Counterclockwise
Rear-left: C / Motor 2
Output 4: function 34
Counterclockwise
Rear-right: B / Motor 4
Output 3: function 36
Clockwise
NOSE / FRONT
View from above
The user confirmed these positions and directions after remapping. Test letters, motor numbers and physical outputs are different identifiers.
Notes: The corrected mapping differs from the original export
Motor test letters indicate test sequence, not output channel numbers. After user-observed motor tests, outputs 2, 3 and 4 were reassigned. The user then confirmed the expected locations and spin directions shown below. This mapping is specific to this physical build and must not be transferred to another assembly.
The recorded protocol is DShot600 (MOT_PWM_TYPE=6); DShot does not use analog ESC throttle calibration. Correct test rotation does not prove a suitable motor idle, full-range ESC behavior, propeller installation, thrust balance or a safe tune. The motor KV, exact motor model, total mass and thrust margin still need a measured record.
Do not reload the old complete hello123 export over the corrected build; it contains the original SERVO output assignments.
The user confirmed these positions and directions after remapping. Test letters, motor numbers and physical outputs are different identifiers.
S08 | ArduPilot: motor connection and motor-test diagrams | https://ardupilot.org/copter/docs/connect-escs-and-motors.html

## Slide 15
AERO / 14
Mission Planner commissioning workflow
Configuration, diagnostics and readback on the ground
Hardware implementation | 26 October 2026
15 / 38
01
Read back the actual FC parameters and save a baseline before changing them.
02
Verify orientation, radio mapping, sensor calibration and current pre-arm messages.
03
Test each motor location and rotation with props removed.
04
Confirm voltage/current measurement, failsafe behavior and manual takeover.
Notes: Configuration, diagnostics and readback on the ground
Mission Planner is used to select firmware target, inspect parameters, calibrate sensors and radio ranges, configure modes, test motors and inspect messages/logs. Configuration changes must be written, followed by any required reboot and a fresh parameter readback. A green UI value is not necessarily proof that every related setting was saved.
The project encountered a loader exception and a range warning during imports. The initial 3-inch pitch/roll acceleration estimate exceeded the documented range; the generated file was corrected to 1800 for ATC_ACC_P_MAX and ATC_ACC_R_MAX. This is a starting estimate, not a flight-derived tune.
Maintain three artifacts: the original export, a reviewed list of intended changes and a fresh post-reboot export. Record firmware version with each. Calibration and motor mapping are aircraft-specific, so a small reviewed patch is preferable to indiscriminate reuse of a donor setup.
Remove props for powered setup and motor testing.
Check board orientation, radio calibration and external compass installation.
Confirm battery sensing before relying on voltage compensation or failsafes.
Inspect pre-arm errors rather than suppressing checks.
S11 | Application repository | https://github.com/rithinreddy0/aero-ground-station
S18 | ArduPilot: initial flight tuning | https://ardupilot.org/copter/docs/setting-up-for-tuning.html

## Slide 16
AERO / 15
MAVLink telemetry contract
Messages consumed by the current adapter
Hardware implementation | 26 October 2026
16 / 38
01
HEARTBEAT: armed state and mode. GLOBAL_POSITION_INT: position and velocity.
02
GPS_RAW_INT: fix, satellites and HDOP. SYS_STATUS: battery state.
03
EKF_STATUS_REPORT: estimator checks; STATUSTEXT: diagnostic messages.
04
Freshness is per message family; a heartbeat cannot substitute for fresh GPS or battery.
Notes: Messages consumed by the current adapter
The adapter only accepts the configured aircraft system/component IDs, defaulting to 1/1. It records monotonic reception times per message family. The application itself sends a GCS heartbeat about once per second with source system 255 and component 190. Those IDs must be considered if other GCS software is also running.
The application checks heartbeat, position, GPS, battery and EKF age separately before movement. Position and heading are decoded from GLOBAL_POSITION_INT; battery percentage is taken from SYS_STATUS when supplied by the FC. Missing values remain unknown rather than being inferred from video OSD.
Message transport does not establish correctness of sensor inputs. Stale, inconsistent or unavailable navigation state must remain visible. Higher message rates are useful only when the RF link can sustain them without excessive buffering and loss.
Message | Fields used
HEARTBEAT | Mode and armed state
GLOBAL_POSITION_INT | Latitude, longitude, relative altitude, speed, heading
GPS_RAW_INT | Fix type and satellite count
SYS_STATUS | Battery voltage and remaining percentage
EKF_STATUS_REPORT | Estimator readiness flags
ATTITUDE / SCALED_PRESSURE | Attitude; available barometer temperature
STATUSTEXT / RADIO_STATUS | Flight messages; link diagnostics
S10 | MAVLink: common message definitions | https://mavlink.io/en/messages/common.html
S11 | Application repository | https://github.com/rithinreddy0/aero-ground-station

## Slide 17
AERO / 16
UML telemetry sequence
State moves from the FC to the interface
Hardware implementation | 26 October 2026
17 / 38
Sensors / FC
ELRS link
GCS adapter
Browser
1. FC emits MAVLink messages
2. Bridge delivers UDP / serial bytes
Filter system/component + timestamp
4. SSE status snapshot
Render ages, instruments and map
Freshness is tracked per message family. A fresh heartbeat alone does not establish fresh GPS, battery or EKF data.
Notes: State moves from the FC to the interface
The browser does not open the aircraft serial port. It subscribes to the local server, which reads snapshots supplied by the telemetry worker. This keeps aircraft communication independent from browser rendering and AI workloads.
A fresh heartbeat only proves that a heartbeat arrived. It cannot substitute for fresh absolute position, valid battery measurement or estimator readiness. All displayed timestamps should be interpreted as reception age, not a measurement of over-air latency.
Freshness is tracked per message family. A fresh heartbeat alone does not establish fresh GPS, battery or EKF data.
S10 | MAVLink: common message definitions | https://mavlink.io/en/messages/common.html
S11 | Application repository | https://github.com/rithinreddy0/aero-ground-station

## Slide 18
AERO / 17
GUIDED movement and control authority
The laptop sends setpoints; the FC stabilizes flight
Hardware implementation | 26 October 2026
18 / 38
01
Pilot selects GUIDED; the operator explicitly leases application control.
02
Fresh telemetry, GPS/EKF, battery, video and bounded limits gate movement.
03
Velocity-only BODY_NED setpoints use mask 0x0DC7; body Z is positive down.
04
The current application does not autonomously arm, take off or land.
Notes: The laptop sends setpoints; the FC stabilizes flight
The implementation sends SET_POSITION_TARGET_LOCAL_NED with MAV_FRAME_BODY_NED and velocity-only mask 0x0DC7 (3527). Its body axes are forward, right and down; an upward command therefore uses negative vertical velocity. The onboard autopilot interprets the request only in a suitable mode and closes the attitude/motor-control loops.
The operator renews a control lease every second; it expires after three seconds. Manual app requests last at most one second and the UI normally asks for 0.5 seconds. Initial application speed is 0.5 m/s. Neither a sent packet nor an HTTP success establishes physical motion; velocity targets do not carry COMMAND_ACK in this usage.
This application does not arm, select GUIDED, take off, land or upload an onboard mission. The operating concept is manual takeoff and stable hover, deliberate GUIDED selection, supervised laptop requests and radio takeover. The model and route generator have no authority to bypass the state gates.
Live control defaults to false. Physical behavior and reliable response require separate SITL/bench/flight acceptance.
S04 | ArduPilot: Guided movement command frames and masks | https://ardupilot.org/dev/docs/copter-commands-in-guided-mode.html
S11 | Application repository | https://github.com/rithinreddy0/aero-ground-station

## Slide 19
AERO / 18
UML command sequence
Requests cross safety gates before reaching the radio
Hardware implementation | 26 October 2026
19 / 38
Pilot / UI
Station gates
MAVLink link
ArduCopter
1. Pilot selects GUIDED; operator leases control
2. Bounded move request / reviewed route
Check mode, GPS, EKF, battery, video, limits
4. Velocity-only BODY_NED setpoint
5. SET_POSITION_TARGET_LOCAL_NED
6. Position / mode telemetry
7. Feedback; stop or pause if invalid
Velocity setpoints have no COMMAND_ACK. The application observes telemetry; the FC closes the stabilization loop.
Notes: Requests cross safety gates before reaching the radio
A UI action first passes local HTTP validation and station policy. An accepted request is encoded into MAVLink, sent over the selected endpoint and interpreted by ArduCopter. The return telemetry path supplies observed position/mode state.
On a pilot mode change away from GUIDED, the application clears its lease and stops issuing velocity requests. A mode change can occur before the next laptop heartbeat is processed; onboard mode handling is therefore the primary authority boundary, not a browser response time.
Velocity setpoints have no COMMAND_ACK. The application observes telemetry; the FC closes the stabilization loop.
S04 | ArduPilot: Guided movement command frames and masks | https://ardupilot.org/dev/docs/copter-commands-in-guided-mode.html
S11 | Application repository | https://github.com/rithinreddy0/aero-ground-station

## Slide 20
AERO / 19
Analog video acquisition
The goggles and telemetry radio do not automatically feed laptop video
Hardware implementation | 26 October 2026
20 / 38
01
Route A: analog VTX -> 5.8 GHz USB/UVC receiver -> laptop.
02
Route B: analog VTX -> RC805 -> composite USB capture -> laptop.
03
The receiver frequency must match the VTX; RC805 only supports its listed eight channels.
04
A goggles memory-card slot is not a live USB video output.
Notes: The goggles and telemetry radio do not automatically feed laptop video
The aircraft camera supplies analog video, optionally through the FC OSD, to the VTX. The iFlight goggles receive the RF image, but no usable AV/USB output was confirmed for this exact model. Their memory-card slot is for recording/storage, not a general live video output.
Two candidate ground routes were discussed. A USB UVC analog receiver combines RF reception and USB conversion. Alternatively, an RC805-style analog receiver provides composite video to a separate EasyCAP-style USB capture adapter. These are candidates, not confirmed purchases or tested capture devices.
The eight-channel RC805 must match an exact supported VTX frequency: 5705, 5685, 5665, 5645, 5885, 5905, 5925 or 5945 MHz. It is not enough that both products say 5.8 GHz. Its listing specifies 12 V power; the capture adapter gets USB power. Check AV connector pinout/cable and actual Windows driver compatibility.
UVC route: VTX -> analog USB receiver -> laptop.
Composite route: VTX -> RC805 -> composite capture -> laptop.
Goggles may receive the same broadcast independently.
No new component prices or stock claims are made in this pack; availability changes and was not re-quoted.
S13 | RC805 candidate receiver specification | https://rcmumbai.com/products/rc-805-5-8ghz-8-channel-av-receiver
S14 | EasyCAP candidate capture-adapter specification | https://probots.co.in/easycap-a072-usb-2-0-audio-video-capture-adapter.html

## Slide 21
AERO / 20
Video formats and timing
Preserve source information and measure complete latency
Hardware implementation | 26 October 2026
21 / 38
01
The analog path has RF, capture, decode, inference and display delays.
02
Use the detector result on its corresponding frame; avoid drawing stale boxes on a newer frame.
03
Uploaded clips provide repeatable tests before a live receiver is available.
04
CPU processing throughput is not the same as end-to-end video latency.
Notes: Preserve source information and measure complete latency
A capture device may expose PAL 720x576 at 25 fps or NTSC 720x480 at approximately 30 fps. These are seller-described modes for the investigated capture adapter, not measured support from a purchased device. Start with the camera/capture standard and verify frame shape, color and stable sync. A higher requested resolution does not add analog source detail.
The application uses OpenCV capture and MJPEG delivery. Its reported capture-frame age begins at the software read, while inference time describes model processing. Neither includes the entire camera-to-VTX-to-RF-to-capture-to-display chain. Measure end-to-end delay with a visible timer or LED comparison.
Capture and inference run independently. Inference processes a recent frame rather than building an ever-growing queue. Annotated detection video uses the analyzed source frame. Raw recording remains available independently; slower inference means skipped source frames, not a claim of full-rate recognition.
S11 | Application repository | https://github.com/rithinreddy0/aero-ground-station
S14 | EasyCAP candidate capture-adapter specification | https://probots.co.in/easycap-a072-usb-2-0-audio-video-capture-adapter.html

## Slide 22
AERO / 21
UML use cases and operator roles
Pilot and rescue operator have distinct responsibilities
Hardware implementation | 26 October 2026
22 / 38
Pilot
manual authority
Rescue operator
review authority
Fly / select mode
View video + telemetry
Review / execute route
Verify lead / save incident
Search assistance does not replace pilot authority or human verification of a potential survivor.
Notes: Pilot and rescue operator have distinct responsibilities
The pilot is responsible for flight readiness, manual control, mode selection and landing. The rescue operator reviews sensor information, proposes a search, validates route limits and verifies candidate incidents. These roles may be held by one trained person in a bench demonstration, but their responsibilities remain distinct.
The app can advise hold or pause a running supervised mission under an explicitly enabled person policy. It cannot declare that the site is obstacle-free or that a detected object is a confirmed survivor. Incident evidence and actions require human interpretation.
Search assistance does not replace pilot authority or human verification of a potential survivor.
S11 | Application repository | https://github.com/rithinreddy0/aero-ground-station

## Slide 23
AERO / 22
Application component architecture
Existing modules and their communication
Hardware implementation | 26 October 2026
23 / 38
HTTP / SSE / MJPEG
validated actions
observe / evidence
bounded requests
record events
<<component>> Browser
map / video / actions
<<component>> FastAPI
auth / validation
<<component>> Station
coordination / gates
Video + YoloDetector
Intelligence
Mission + navigator
Telemetry / pymavlink
Store + Recorder
SQLite / JPEG / AVI
Independent workers keep capture, inference and telemetry from waiting on one another. The station owns policy decisions.
Notes: Existing modules and their communication
FastAPI validates requests and serves the interface. Station coordinates telemetry, video, movement gates, mission execution, intelligence, recording and storage. The browser receives status through SSE and video through MJPEG; write actions carry a random per-process token and are restricted by same-origin and Host checks.
The software remains local by default. Optional online map layers make network requests for background tiles, but detection and the bounded intent planner do not need a cloud model. Do not expose the control server to a public interface without a separate access-control design. Incoming UDP MAVLink is not authenticated by this adapter.
Independent workers keep capture, inference and telemetry from waiting on one another. The station owns policy decisions.
S11 | Application repository | https://github.com/rithinreddy0/aero-ground-station

## Slide 24
AERO / 23
UML runtime class diagram
Implementation classes and data ownership
Hardware implementation | 26 October 2026
24 / 38
settings
owns
owns
owns
detection snapshots
Station
start(), state(), loop()
Config
validated settings
Video / YoloDetector
capture(), predict()
Mission / Telemetry
tick(), send_velocity()
Store / Recorder
add(), save_mission()
Intelligence
update(), snapshot()
This is a condensed implementation class view; function names reflect the Python application rather than hypothetical modules.
Notes: Implementation classes and data ownership
Config validates operating mode, flight envelope and detector options. Telemetry owns MAVLink decoding. Video owns capture and analysis workers. YoloDetector adapts model output into normalized boxes. Intelligence tracks image-space candidates. Mission computes bounded waypoint velocity; Store and Recorder preserve evidence.
The class view is intentionally condensed. Mission and Telemetry are separate classes, as are Store and Recorder, even where grouped in a diagram box to retain readability. The editable Mermaid source contains the individual ownership relationships for a more detailed rendering.
This is a condensed implementation class view; function names reflect the Python application rather than hypothetical modules.
S11 | Application repository | https://github.com/rithinreddy0/aero-ground-station

## Slide 25
AERO / 24
AURA model and enhancement integration
Aerial model, lightweight alternative and explicit processing choices
Hardware implementation | 26 October 2026
25 / 38
01
AURA integration includes the VisDrone model and a configurable lightweight YOLO alternative.
02
CLAHE and hybrid enhancement are available; choose processing explicitly.
03
The saved checkpoint does not demonstrate a separately integrated CBAM or Zero-DCE model.
04
Recorded CPU timings and one detection example are observations, not accuracy validation.
Notes: Aerial model, lightweight alternative and explicit processing choices
The team integration is pinned to upstream commit d50829119b598e5b32b352f384fdd25aca367f08. A downloader verifies SHA-256 checksums before using local checkpoints. The integrated models are YOLOv8m VisDrone and YOLO26n COCO. The recorded VisDrone checkpoint has no verified CBAM blocks; the pack does not claim CBAM inference.
VisDrone labels pedestrian and people are mapped to the existing person policy while retaining their original labels. Classical CLAHE and FPV hybrid enhancement are optional model-input transformations. They are not a learned accuracy guarantee. Original imagery remains important evidence for operator comparison.
Optional OSD exclusion is a calibrated geometric post-filter. It can hide real objects overlapping telemetry graphics, so it is off by default and requires a matching profile. The included profile applies to one source layout, not every camera. Detector failures are surfaced explicitly; a selected broken YOLO model is not silently replaced by HOG.
CPU FP32 is the installed baseline; compatible CUDA use is configurable.
The earlier recorded CPU timing was roughly 230-320 ms per warmed result.
That observation is not a benchmark across all clips or a measure of aerial accuracy.
S11 | Application repository | https://github.com/rithinreddy0/aero-ground-station
S12 | Team AURA source, pinned integration revision | https://github.com/7-Azhar/major_project/tree/d50829119b598e5b32b352f384fdd25aca367f08

## Slide 26
AERO / 25
Uploaded-video test workflow
Local video testing does not open a drone-control connection
Hardware implementation | 26 October 2026
26 / 38
Operator / UI
FastAPI
Video / YOLO
Tracker / UI
1. Upload video + choose model
Check demo mode, token, size and decoding
3. Swap source; clear lease and old tracks
Read latest frame; enhance; infer
5. Normalize classes and timestamp boxes
6. Annotated MJPEG for same source frame
7. Candidate evidence + operator review
Uploaded footage is a local test input. Aircraft telemetry remains simulated and no MAVLink connection is opened.
Notes: Local video testing does not open a drone-control connection
The operator chooses a local file, detector and enhancement, then uploads through the existing app. The server accepts supported containers up to 500 MB, checks authentication and decodability, and only permits source replacement in demo mode. Recordings must be stopped before swapping the source.
A source change clears the control lease and old person tracks and pauses any simulated mission. Playback loops at the source rate; AI uses the newest available frames. Annotated MJPEG preserves frame-to-box alignment and reports inference age. The displayed flight telemetry in this mode is simulated, even though the video and model inference are real.
Uploaded footage is a local test input. Aircraft telemetry remains simulated and no MAVLink connection is opened.
S11 | Application repository | https://github.com/rithinreddy0/aero-ground-station
S12 | Team AURA source, pinned integration revision | https://github.com/7-Azhar/major_project/tree/d50829119b598e5b32b352f384fdd25aca367f08

## Slide 27
AERO / 26
Person evidence, tracking and decisions
Temporal persistence reduces single-frame triggers
Hardware implementation | 26 October 2026
27 / 38
01
Track people over distinct source frames; require persistence before confirming a lead.
02
IoU association and expiry rules reduce repeated or isolated detections.
03
Human review is still required; detections are not confirmed survivors.
04
A detected person can pause a mission; recovery remains an explicit operator decision.
Notes: Temporal persistence reduces single-frame triggers
Normalized boxes are associated using image-space intersection over union. The existing tracker requires three distinct matched detection frames before calling a track persistent. A track expires after about 1.5 seconds without updates; a confirmed candidate must also have been seen recently, within about 0.8 seconds.
Advisory mode presents evidence. The optional pause-on-person policy pauses an active mission when a persistent candidate is present and creates an incident with a cooldown. It does not identify the person, infer injuries or establish a victim position. The recorded aircraft coordinates are context about the camera platform.
Slow CPU inference, analog interference, high altitude, small objects and camera angle can all reduce useful evidence. Counted boxes across frames are not unique people. Camera calibration, synchronized pose and terrain/ranging data would be needed for defensible image-to-ground geolocation.
Do not interpret HOG scores as probabilities.
Keep original class labels and source frame IDs in review evidence.
Auto-pause recovery remains latched until explicit operator action.
S11 | Application repository | https://github.com/rithinreddy0/aero-ground-station
S12 | Team AURA source, pinned integration revision | https://github.com/7-Azhar/major_project/tree/d50829119b598e5b32b352f384fdd25aca367f08

## Slide 28
AERO / 27
Mission activity and route feedback
GPS waypoints are followed by a laptop controller
Hardware implementation | 26 October 2026
28 / 38
yes
no
done
fault
Draft search route
Validate route / review
Flight + lease gates pass?
Stream bounded velocity
Pause / reject
wait for operator
Complete / cancel
Fault, person-policy and pilot events pause the route. Human review and an explicit resume action are required.
Notes: GPS waypoints are followed by a laptop controller
The app validates 1-100 WGS84 points with relative altitude and hold time against its configured radius/ceiling. Its local grammar can propose search grids, perimeters, orbit-like routes and bounded movements. It is a deterministic intent parser, not an unrestricted language-model pilot.
The navigator computes north/east/vertical error to the next point, limits speed, rotates horizontal velocity by current heading and streams body-frame requests. Arrival uses approximately 0.6 m horizontal and 0.4 m altitude tolerances in the present implementation. Those tolerances require real positioning-performance assessment; ordinary GPS must not be assumed to achieve them reliably.
This route is not an onboard AUTO mission. The app does not upload takeoff/land items, provide obstacle avoidance or evaluate terrain clearance.
Fault, person-policy and pilot events pause the route. Human review and an explicit resume action are required.
S11 | Application repository | https://github.com/rithinreddy0/aero-ground-station

## Slide 29
AERO / 28
Mission state and recovery
Pause is a latched state, not automatic fault recovery
Hardware implementation | 26 October 2026
29 / 38
validate / load
start + gates
fault / pause / pilot
explicit resume + gates
finish / cancel
edit / reload
empty
ready
running
paused
completed / cancelled
Editing a paused route loads a new ready plan. Start begins at point one; Resume continues the paused route.
Notes: Pause is a latched state, not automatic fault recovery
Loading a validated route creates ready state. Start begins at the first point. Operator pause, unavailable prerequisites or person policy can produce paused state. Resume requires current prerequisites and an explicit request; cancelling terminates the current route execution.
Editing a paused plan creates a new ready plan. Automatic return of a good signal does not mean the earlier action should resume. The distinction is important after pilot intervention, low battery, video loss or a person lead that requires review.
Editing a paused route loads a new ready plan. Start begins at point one; Resume continues the paused route.
S11 | Application repository | https://github.com/rithinreddy0/aero-ground-station

## Slide 30
AERO / 29
Incident storage and data model
Evidence is stored locally with explicit provenance
Hardware implementation | 26 October 2026
30 / 38
kind = incident
snapshot filename
execution events
events table
id / UTC time / kind / JSON
missions table
id / name / plan JSON
incident event payload
note / aircraft position / filename
Local files
JPEG / AVI / uploads
Incidents are JSON payloads in events, not a separate incident table. Positions describe the aircraft, not an inferred victim.
Notes: Evidence is stored locally with explicit provenance
SQLite stores events as id, UTC time, kind and JSON payload, and stores missions as id, name and plan JSON. Incident entries can reference a JPEG snapshot and the aircraft position available at that time. The raw AVI recorder runs independently with bounded duration/storage; video uploads remain separate local files.
The application supports event/log export and route JSON/GeoJSON/WPL exchange with defined limitations. A WPL export is not proof that it was uploaded to or accepted by a vehicle. Data retention is manual, and uploaded footage can contain people or locations, so sharing the code repository is different from publishing the local evidence directory.
Incidents are JSON payloads in events, not a separate incident table. Positions describe the aircraft, not an inferred victim.
S11 | Application repository | https://github.com/rithinreddy0/aero-ground-station

## Slide 31
AERO / 30
Safety gates and onboard failsafe layers
Protective logic belongs both onboard and in the application
Hardware implementation | 26 October 2026
31 / 38
01
Onboard protection: arming checks, radio failsafe, GCS failsafe and battery actions.
02
Application protection: message freshness, video age, lease, mode, GPS/EKF and motion bounds.
03
Pilot intervention or a protective event pauses route execution.
04
Evaluate link-loss behavior and mode recovery on the actual configured aircraft.
Notes: Protective logic belongs both onboard and in the application
App live control requires enabled configuration, an operator lease, fresh heartbeat/position/GPS/battery/EKF, GUIDED mode, armed state, a 3D fix, estimator readiness, sufficient battery, valid altitude/radius and fresh video. Current age limits are 2.5 seconds for core telemetry and 1 second for video. Defaults are 0.5 m/s, 30 m altitude and 50 m radius.
Onboard RC, GCS, battery and estimator failsafes operate independently from those application gates. The historical settings include FS_THR_ENABLE=1, FS_GCS_ENABLE=1, FS_GCS_TIMEOUT=5, FS_OPTIONS=16 and GUID_TIMEOUT=3. FS_OPTIONS=16 permits continued pilot-controlled operation on GCS loss; it is not a general instruction to continue GUIDED flight.
RC loss and GCS loss are separate failure events even when they share an RF system. A disarmed test that produces a failsafe message establishes detection, not the resulting airborne trajectory. Other GCS heartbeats can affect a laptop-loss test. Verify behavior with a controlled procedure and logs.
Application home/radius checks are not a replacement for the onboard fence. The project fence parameters were staged with FENCE_ENABLE=0.
S05 | ArduPilot: GCS failsafe | https://ardupilot.org/copter/docs/gcs-failsafe.html
S06 | ArduPilot: radio failsafe | https://ardupilot.org/copter/docs/radio-failsafe.html
S11 | Application repository | https://github.com/rithinreddy0/aero-ground-station

## Slide 32
AERO / 31
Parameter register and provenance
Historical changes grouped by purpose; read back before relying on them
Hardware implementation | 26 October 2026
32 / 38
01
Historical files document changes; they are not a complete current FC snapshot.
02
Groups cover frame/motors, RC modes, GPS/UARTs, telemetry and onboard protection.
03
Later motor mapping and tuning corrections differ from the first exported baseline.
04
Read back the aircraft before relying on any parameter value in this report.
Notes: Historical changes grouped by purpose; read back before relying on them
The original hello123 export contained 1,098 entries. Subsequent small files changed battery protection, telemetry streams, modes, navigation speeds, fence limits, motor mapping, GPS baud and initial tuning. The earlier combined setup patch did not contain later motor/GPS/tuning changes. These files must not be treated as interchangeable complete current-state exports.
A fresh FC parameter export should be compared with this register and the physical build. The pack deliberately does not provide a new flight-ready all-parameter import because current GPS readiness, sensor calibration and airborne behavior are not verified.
Purpose | Recorded project values
Battery sensing | Monitor 4; volt pin 10; current pin 12; multiplier 11; scale 39.4
Battery protection | Capacity 650; low 14.4 V / RTL; critical 14.0 V / Land; arm 14.7 V
GPS / ELRS | SERIAL5=GPS at 115200; SERIAL6=MAVLink2 at 460800
Telemetry | MAV2 EXT_STAT/POSITION/EXTRA1-3/RAW_SENS/RC_CHAN = 1 Hz
Speed / fence staging | Loiter 2 m/s; WP 1 m/s; RTL 2 m/s; radius 50 m; max 30 m; fence OFF
Initial tuning | Pitch/roll accel 1800; yaw 333; gyro filter 115 Hz; thrust expo 0.41
Preserve | Calibration, verified motor map and radio mapping; no skipped arming checks
MOT_BAT_VOLT_MIN=13.2 V is a compensation bound, not the chosen critical landing threshold. Do not confuse the two.
S11 | Application repository | https://github.com/rithinreddy0/aero-ground-station

## Slide 33
AERO / 32
Commissioning and field workflow
Progress through evidence-based acceptance stages
Hardware implementation | 26 October 2026
33 / 38
01
Bench acceptance: power, wiring, sensors, motor mapping, RC, telemetry and failsafes.
02
Flight acceptance: supervised stability, vibration, hover current, GNSS quality and takeover.
03
Application acceptance: bounded movement, stale-data stops, video loss and incident policy.
04
Progress only after the preceding stage has recorded evidence.
Notes: Progress through evidence-based acceptance stages
Begin with a complete build inventory, backups and propellers removed. Establish correct board orientation, radio calibration, motor order/direction, sensor installation and valid battery measurement. Resolve GPS communication and navigation readiness before evaluating position-dependent modes.
Next verify USB telemetry, then wireless telemetry using the actual bridge. Validate video capture separately from detection. Use SITL or an appropriate controlled rig for movement-axis interpretation, command timeout and mode-takeover behavior. Only after ground acceptance should a trained pilot conduct a manual outdoor hover and log review in a suitable clear area.
For application flight, establish a safe manual hover, select GUIDED deliberately, review the route and enable the control lease. Keep the pilot ready for mode takeover. After a fault, pause and assess rather than automatically resuming. Land through the pilot/onboard mode procedure and review logs, evidence, battery consumption and latency.
Ground acceptance: electrical, mechanical, sensor, RC and telemetry checks.
Flight acceptance: stability, vibration, hover current, GPS quality, takeover and protective behavior.
Application acceptance: freshness gates, bounded movement, video loss and incident policy.
S11 | Application repository | https://github.com/rithinreddy0/aero-ground-station
S18 | ArduPilot: initial flight tuning | https://ardupilot.org/copter/docs/setting-up-for-tuning.html

## Slide 34
AERO / 33
Test matrix and remaining measurements
Software tests do not certify physical flight behavior
Hardware implementation | 26 October 2026
34 / 38
01
The last recorded suite had 46 passing tests; this is historical software evidence.
02
Repeatable clip tests cover upload, model selection, frame alignment and review.
03
Measure real GNSS quality, RF range, voltage/current calibration and full video latency.
04
No field search accuracy, endurance or autonomous-flight certification is claimed.
Notes: Software tests do not certify physical flight behavior
The last recorded automated run reported 46 passing tests. It covered control gating, MAVLink encoding/decoding, route validation, tracking, upload behavior and local evidence generation. Actual inference on one team FPV sample established that the model loads and returns detections, not its precision, recall or performance over disaster scenes.
For every physical acceptance test, record configuration/version, setup, expected result, observed result, pass/fail and evidence filename. Test one independent fault at a time. Record separate timings for camera-to-display delay, inference throughput, command-to-observed-response delay and mode takeover.
Test | Current evidence / next measurement
Motor mapping / mode selection | User confirmed on bench; retain a labelled build record
RC-loss detection | Message appeared and cleared while disarmed
GPS / compass | Fix and level-heading verification unresolved
Battery | Plausible 14.95 V once shown; external comparison/current still needed
AI upload | Software/browser verified; task accuracy unmeasured
Wireless command / GCS loss | Controlled link-loss response and logs still required
Manual flight / endurance | Stable hover, vibration, power and duration not demonstrated here
S11 | Application repository | https://github.com/rithinreddy0/aero-ground-station

## Slide 35
AERO / 34
Troubleshooting by subsystem
Use a discriminating check before changing parameters
Hardware implementation | 26 October 2026
35 / 38
01
GPS: check fix/satellites/HDOP, supply, crossed UART wires and serial configuration.
02
Radio failsafe: verify the transmitter, live RC input and receiver link status.
03
Battery: compare FC voltage against a meter; do not bypass pre-arm protection.
04
Video: separate RF/frequency problems from USB driver, device selection and AI issues.
Notes: Use a discriminating check before changing parameters
GPS: distinguish no receiver data from a detected receiver with poor fix. Confirm stable supply, TX/RX crossing, UART5 assignment and fresh GPS telemetry; then test antenna-up outdoors away from interference. Obtain satellite count/fix/accuracy rather than relying on LED colors. A compass can be detected while GPS serial data is still wrong.
Battery: USB-only near-zero pack voltage is expected when the battery input is unpowered. With a pack connected, compare against a meter/charger before adjusting scale. A low-arming-voltage error is not a reason to bypass arming checks. Radio: verify ELRS connection, moving channel bars and the transition into/out of failsafe.
Laptop/video: close competing applications before opening a COM port or camera. Check the exact RF video frequency, capture standard, data cable and driver. An HDMI-only adapter does not accept composite video. AI: verify dependencies, local weights/checksums, source decodability and warm-up status; test the lightweight model if processing cannot keep up.
Preserve one known-good baseline and change one variable per diagnostic step.
Use current STATUSTEXT and FC logs; old UI messages can outlast a transient condition.
Do not infer a live GPS position from map centering or cached coordinates.
S03 | Flywoo: GOKU GM10 Mini V3 GPS specifications | https://flywoo.net/products/goku-gm10-mini-v3-gps
S11 | Application repository | https://github.com/rithinreddy0/aero-ground-station

## Slide 36
AERO / 35
Disaster-management extensions
Feasible additions and their boundaries
Hardware implementation | 26 October 2026
36 / 38
01
Start with offline incident review, operator notes, mission replay and exportable evidence.
02
An ESP32 plus DFPlayer/amplifier can play prerecorded messages; a bare ESP32 is not a loudspeaker.
03
Payload power, mass, mounting and RF effects need a separate bench and flight evaluation.
04
Thermal imaging, relay networking and precise survivor geolocation are future integrations.
Notes: Feasible additions and their boundaries
The easiest software additions are operator-confirmed incident status, priority, notes, revisits and a mission evidence report. A future coverage view should state its assumptions; the aircraft track alone does not prove the camera observed every point in a search area.
A small prerecorded-announcement prototype could use ESP32/XIAO, DFPlayer Mini, storage and a lightweight speaker. An alternative is an I2S amplifier with an ESP32S3. Send a selected message ID over a separately engineered command path rather than trying to stream voice through the existing telemetry link. Measure intelligibility against propeller noise and verify regulator/payload margin.
A stationary ground SOS unit avoids adding aircraft mass and can use a button, acknowledgement light and optional microphone. Marker release or supply delivery would need payload/thrust, release-output and safe-drop testing. None of these add-ons are installed or integrated in the current application.
Prioritize incident workflow before extra airborne payload.
Treat long-range Wi-Fi, airborne speech recognition and live two-way audio as research tasks.
Document each proposed addition separately from the confirmed build.
S11 | Application repository | https://github.com/rithinreddy0/aero-ground-station
S15 | DFRobot: DFPlayer Mini audio module | https://www.dfrobot.com/product-1121.html/
S16 | Seeed Studio: XIAO ESP32S3 family | https://wiki.seeedstudio.com/xiao_esp32s3_getting_started/

## Slide 37
AERO / 36
Limitations, glossary and viva questions
Explain the design without overstating capability
Hardware implementation | 26 October 2026
37 / 38
01
MAVLink is the message protocol; ELRS is the RF transport; ArduCopter is the autopilot.
02
GPS measures position; the compass measures magnetic heading; EKF fuses sensor evidence.
03
AI boxes suggest candidates. Aircraft coordinates are not the person’s ground coordinates.
04
Explain the confirmed prototype, its remaining tests and its limits during the viva.
Notes: Explain the design without overstating capability
Current limits: unresolved physical GPS readiness, unverified end-to-end live video acquisition, no onboard mission upload, no automatic arming/takeoff/landing, no obstacle avoidance, no exact victim geolocation and no validated rescue-scene accuracy benchmark. AI candidates require human review. A smartphone/ESP32 addition does not remove those limits.
AIO means all-in-one board; FC is flight controller; ESC is electronic speed controller; GCS is ground control station; GNSS is satellite navigation; EKF is the state estimator; UART is a serial interface; MAVLink is a message protocol; ELRS is the RC/RF ecosystem; VTX/VRX are video transmitter/receiver; OSD is an image overlay; UVC is a USB video-device interface.
Why both Mission Planner and our app? Mission Planner commissions and diagnoses the FC; our app adds search/vision/incident workflows. Where does AI run? On the laptop. Why separate video and telemetry? They use different sensors, links and interfaces. Why does GPS matter? Current GUIDED navigation uses position/heading feedback. Why is a person box not a coordinate? Projection needs calibrated geometry, synchronized pose and terrain/ranging.
S11 | Application repository | https://github.com/rithinreddy0/aero-ground-station

## Slide 38
AERO / 37
References and source register
Trace implementation details to project evidence and primary documentation
Hardware implementation | 26 October 2026
38 / 38
01
Primary references: ArduPilot board, motor, Guided-control and failsafe documentation.
02
Transport references: ExpressLRS native MAVLink and MAVLink common messages.
03
Implementation references: application repository and pinned team AURA revision.
04
All 18 links and detailed section notes are included in the PDF and editable source pack.
Notes: Trace implementation details to project evidence and primary documentation
Primary evidence: this project conversation, its screenshots and user-reported bench results; the hello123 parameter export and later commissioning patches; the application Python/JavaScript source; docs/COMMISSIONING.md and docs/AURA_INTEGRATION.md; the 16 October software verification record.
Documentation assembled on 26 October 2026. Board wiring and firmware behavior must be checked against the exact installed revision. Source links are references, not evidence that the documented hardware was purchased or that all optional firmware features are available. Keep a post-reboot FC export and measured acceptance record with the final report.
S01 | ArduPilot: SpeedyBee F405 AIO board support | https://ardupilot.org/copter/docs/common-speedybeef405aio.html
S02 | ExpressLRS: native MAVLink setup and laptop bridging | https://www.expresslrs.org/software/mavlink/
S03 | Flywoo: GOKU GM10 Mini V3 GPS specifications | https://flywoo.net/products/goku-gm10-mini-v3-gps
S04 | ArduPilot: Guided movement command frames and masks | https://ardupilot.org/dev/docs/copter-commands-in-guided-mode.html
S05 | ArduPilot: GCS failsafe | https://ardupilot.org/copter/docs/gcs-failsafe.html
S06 | ArduPilot: radio failsafe | https://ardupilot.org/copter/docs/radio-failsafe.html
S07 | ArduPilot: battery failsafe | https://ardupilot.org/copter/docs/failsafe-battery.html
S08 | ArduPilot: motor connection and motor-test diagrams | https://ardupilot.org/copter/docs/connect-escs-and-motors.html
S09 | ArduPilot: radio mode-switch configuration | https://ardupilot.org/copter/docs/common-rc-transmitter-flight-mode-configuration.html
S10 | MAVLink: common message definitions | https://mavlink.io/en/messages/common.html
S11 | Application repository | https://github.com/rithinreddy0/aero-ground-station
S12 | Team AURA source, pinned integration revision | https://github.com/7-Azhar/major_project/tree/d50829119b598e5b32b352f384fdd25aca367f08
S13 | RC805 candidate receiver specification | https://rcmumbai.com/products/rc-805-5-8ghz-8-channel-av-receiver
S14 | EasyCAP candidate capture-adapter specification | https://probots.co.in/easycap-a072-usb-2-0-audio-video-capture-adapter.html
S15 | DFRobot: DFPlayer Mini audio module | https://www.dfrobot.com/product-1121.html/
S16 | Seeed Studio: XIAO ESP32S3 family | https://wiki.seeedstudio.com/xiao_esp32s3_getting_started/
S17 | SpeedyBee manufacturer board manual | https://spcdn.speedybee.cn/cdn/58507926851031040.pdf
S18 | ArduPilot: initial flight tuning | https://ardupilot.org/copter/docs/setting-up-for-tuning.html
S01 | ArduPilot: SpeedyBee F405 AIO board support | https://ardupilot.org/copter/docs/common-speedybeef405aio.html
S02 | ExpressLRS: native MAVLink setup and laptop bridging | https://www.expresslrs.org/software/mavlink/
S03 | Flywoo: GOKU GM10 Mini V3 GPS specifications | https://flywoo.net/products/goku-gm10-mini-v3-gps
S04 | ArduPilot: Guided movement command frames and masks | https://ardupilot.org/dev/docs/copter-commands-in-guided-mode.html
S05 | ArduPilot: GCS failsafe | https://ardupilot.org/copter/docs/gcs-failsafe.html
S06 | ArduPilot: radio failsafe | https://ardupilot.org/copter/docs/radio-failsafe.html
S07 | ArduPilot: battery failsafe | https://ardupilot.org/copter/docs/failsafe-battery.html
S08 | ArduPilot: motor connection and motor-test diagrams | https://ardupilot.org/copter/docs/connect-escs-and-motors.html
S09 | ArduPilot: radio mode-switch configuration | https://ardupilot.org/copter/docs/common-rc-transmitter-flight-mode-configuration.html
S10 | MAVLink: common message definitions | https://mavlink.io/en/messages/common.html
S11 | Application repository | https://github.com/rithinreddy0/aero-ground-station
S12 | Team AURA source, pinned integration revision | https://github.com/7-Azhar/major_project/tree/d50829119b598e5b32b352f384fdd25aca367f08
S13 | RC805 candidate receiver specification | https://rcmumbai.com/products/rc-805-5-8ghz-8-channel-av-receiver
S14 | EasyCAP candidate capture-adapter specification | https://probots.co.in/easycap-a072-usb-2-0-audio-video-capture-adapter.html
S15 | DFRobot: DFPlayer Mini audio module | https://www.dfrobot.com/product-1121.html/
S16 | Seeed Studio: XIAO ESP32S3 family | https://wiki.seeedstudio.com/xiao_esp32s3_getting_started/
S17 | SpeedyBee manufacturer board manual | https://spcdn.speedybee.cn/cdn/58507926851031040.pdf
S18 | ArduPilot: initial flight tuning | https://ardupilot.org/copter/docs/setting-up-for-tuning.html